## Slide 1
USB A - USB B Cable
Power Supply
14v - 18v
1 to 2 Amp
depending on scale
Motor Shield sits on top of the UNO.
Ensure pins line up with sockets and go fully home.
Cut the trace between the two Vin Connect solder pads on the underside of the shield.
Track connections or DCC Bus
Programming Track
Micro USB Power Supply
Raspberry Pi Revision 4
Arduino UNO
Arduino Motor Shield Revision 4
Link Pins
12 & 10
Link Pins
13 & 5
Micro
SD Card
Wall power outlet
Use a suitably sized solid core wire for both links. You want a good connection.